## Slide 1
Click to add text

## Slide 2: RECORDERS

## Slide 3
Principle of operation with applications of Recorders :
Strip chart recorder, Galvanometric type
Magnetic type rercorder
Digital recorders
Advantages disadvantages and applications of Digital recorders

## Slide 4: Introduction
After collecting information about the state of some process, the next consideration is how to present it in a form where it can be readily used and analysed.
This chapter, therefore, starts by covering the techniques available to either display measurement data for current use or record it for future use.

## Slide 6
Measuring instruments (i.e. secondary instruments) may be classified according to their function as:
1. Indicating instruments
2. Integrating instruments
3. Recording instruments

## Slide 7
Indicating instruments: “Indicating instruments are those which indicate the magnitude of an electrical quantity at the time when it is being measured.”
Their indications are given by a pointer moving over calibrated dial.
Example: Ordinary voltmeters, ammeters and wattmeter’s, etc.
2. Integrating instruments: “Integrating instruments are those which measure and register by a set of dials and pointer either the total quantity of electricity (In amp-hours) or the total amount of electrical energy (in watt-hours or kWh) supplied to a circuit in a given time.”
Example: The ampere-hour meters and energy (watt-hour) meters

## Slide 8
3. Recording instruments: “Recording instruments are those which give a continuous record of the variation of the electrical quantity over a selected period of time.”
The moving system of the instruments carries an inked pen which rests lightly on a chart or graph, wrapped over a drum moving with a slow uniform speed. The motion of the drum is in a direction perpendicular to that of the pointer. The path traced out by the pen indicates of the electrical quantity.
Example: Recording voltmeter and ammeter.
Uses: These instruments are generally used in supply stations (i.e. power houses) where continuous information is required.

## Slide 9
A recorder is a device whose function is to record the value of a quantity as it is being measured.
Recording preserves the experimental data in a manageable and usable form.
A recording system is very useful in industries as
(i) it preserves information which could be obtained at an instant from indicating instruments and
(ii) it gives information about waveforms and transient behavior or phase relations in different parts of a circuit.

## Slide 10
The indicating instrument records a continuous reading, but they require an observer for continuously observing the variations in readings.
The example of the recording instrument is obtained by improving the construction of an indicating instrument. The indicating instrument is converted into a recording instrument by replacing their pointer with the light arm ink pen.
The ink pen is deflected for recording the readings on the graph paper. The pen is continuously rotated on the drum at the constant speed. The path traced by the pen gives a continuous reading of the variant physical quantity.
The magnitude of the quantity is read from the traced chart. The instruments are used in the power stations where continuous reading is required.

## Slide 11
The recording instruments take readings of the physical quantities in the form of the graph. It also records the variation of the quantities concerning the time. The voltmeter, thermoscope, ECG machine, galvanometer recorder are the examples of the recording instrument.

## Slide 12
A recorder records both electrical and non-electrical quantities as a function of time or relates two signals to each other.
Electrical quantities, such as current voltage etc can be recorded directly while non-electrical quantities, such as pressure, temperature, speed etc are recorded indirectly by first converting them into the form of electrical signal with the help of sensors and transducers.

## Slide 14
When working with the analog system the analog recording techniques should be used while working with a digital system, digital recording devices should be used.
Recording devices are of two types namely: (i) analog recorders and (ii) digital recorders.

## Slide 15: Types of recorders
Electronic recorders may be classified as
i. Analog recorders
ii. Digital recorders
 Analog recorders dealing with analog systems can be classified as
i. Graphic recorders
ii. Oscillographic recorders
iii. Magnetic Tape recorders
 Digital recorders dealing with digital output can be classified as
i. Incremental Digital recorders
ii. Synchronous Digital recorders

## Slide 16
Analog recorders may be classified as:
1. Graphic Recorder
(i) Strip Chart Recorder
(ii) Circular Chart Recorder
(iii) X-Y Recorders
(a) Analog X-Y Recorder
(b) Digital X-Y Recorder
2. Oscillographic Recorder
3. Magnetic Tape Recorder
All of these generally contain a built-in measuring apparatus as well as a recording mechanism.
This gives recorders the capability of receiving electrical signals from detectors or sensors and converting their magnitudes in to a permanent record.

## Slide 18: Recorder Selection:

## Slide 21: Graphic Recorder
11.3 Graphic Recorder
The graphic instrument displays and stores the physical quantity being measured.
It uses basic elements as chart paper for displaying and storing the quantity and pen for marking the variation in physical quantity. The pen is also called stylus. There are three types of graphic recorders:
1. Strip Chart Recorder
2. Circular Chart Recorder
3. X-Y Tape recorder

## Slide 22
Chart recorders are built in three primary formats.
Strip chart recorders have a long strip of paper that is ejected out of the recorder.
Circular chart recorders have a rotating disc of paper that must be replaced more often, but are more compact and amenable to being enclosed behind glass.
Roll chart recorders are similar to strip chart recorders except that the recorded data is stored on a round roll, and the unit is usually fully enclosed.

## Slide 23: Strip Chart Recorder
A chart recorder is an electromechanical device that records an electrical or mechanical input trend onto a piece of paper (the chart).
Chart recorders may record several inputs using different color pens and may record onto strip charts or circular charts.
Chart recorders may be entirely mechanical with clockwork mechanisms or electro-mechanical with an electrical clockwork mechanism for driving the chart (with mechanical or pressure inputs) or entirely electronic with no mechanical components at all (a virtual chart recorder).

## Slide 24
The strip chart recorder often used for the application which require monitoring the quantity.
A roll of paper is continuously moved under the pen and a continuous record is maintained.
Strip chart recorders are generally multirange voltmeter with a speed range selector to control the paper feed.
A strip-chart recorder plots one or more parameters as a function of time.
A strip is a ribbon of paper moved through the instrument at uniform speed by an electric motor.

## Slide 28
Fig. 11.1 shows the basic block diagram of strip chart recorder.
The basic element of this recorder is pen for making and chart paper for recording data.
The quantity to be measured is given as to the input to the range selector. The range selector switch keeps data within the limit.
The stylus moved along the calibrated scale in accordance with input data.
To get proper record of input data signal conditioning block is used which gives proper input signal along calibrated scale.
The chart paper moves vertically at a uniform speed. The speed selector selects the required speed of the chart paper movement. General diagram of strip char recorder is shown in Fig. 11.2.

## Slide 29
A strip chart consists of the following:
(a) Chart/Paper Long graph paper kept on two rollers, lower roller drags the paper vertically with the help of a motor.
(b) Chart Speed Selector Controls the speed of the roller at some specified speed selected by the operator and hence controls the time scale.
(c) Range Selector Amplifier or attenuator which is to be adjusted according to the amplitude level of physical variable. If the physical variable to be recorded is of very low amplitude then it needs to be amplified with proper gain. The gain value is adjusted by selecting proper range.

## Slide 30
(d) Stylus Driving System Moves the stylus in proportion to the physical variable to be recorded, in most recorders, a synchronous motor is used for driving the paper.
(e) Stylus Create marking/impression on the moving graph paper [most recorders use a pointer attached to the stylus, which (pointer) moves over a calibrated scale thus showing instantaneous value of the quantity being measured].

## Slide 40
2. Rectilinear system/Potentiometric recorders:
It is notices that a line of constant time is perpendicular to the time axis and therefore this system produces a straight line across the width of the chart.
Hence the stylus is actuated by a drive cord over pulleys to produce the forward and reverse motion as determined by the drive mechanism.
The stylus may be actuated by a self-balancing potentiometer system, a photoelectric deflection system, a photoelectric potentiometer system, or a bridge balance system.
This system is usually used with thermal or electric wiring

## Slide 43
Most recorders use a pointer attached to the stylus. This pointer moves over a calibrated scale giving the instantaneous value of the quantity being recorded.
Paper drive system: The paper drive system should move the paper at a uniform speed. A spring would may be used but in most of the recorder a synchronous motor (Stepper motor to be exact) is used for driving the paper
Chart speed: Chart speed is a term used to express the rate at which the recording paper in a strip chart recorder moves.
It is expressed in in/s or mm/s and is determined by mechanical gear trains. If –the chart speed is known, the period of the recorded signal can be calculated as

## Slide 44
Strip chart recorders are commonly used in laboratory as well as process measurement applications. Modern strip chart recorders have the facility of
(i) Simultaneous recording and display of multipoint data
(ii) Universal input: The recorders accept wide range of dc voltage, all common thermocouple and RTD. Often these ranges can be programmed for each channel.
(iii) Universal power voltage of 100 V ac to 240 V ac, 50/60 Hz
(iv) Alarm Display/Printings
(v) Chart illumination convenient to confirm printed signal in the night or in dark places.

## Slide 45: Advantages of Strip Chart Recorder
The strip chart recorder has a number of advantages. Some of the important ones are given below :
1. Relatively large amount of paper can be inserted at one time.
2. Data conversion is easier with rectangular coordinates system
3. The rate of movement of the chart can be easily changed.
4. More than one separate variable can be recorded on a strip chart

## Slide 46
11.6 Disadvantages of Strip Chart Recorder
Strip Chart recorder has some disadvantages also. These are given below:
1. Mechanism is more complicated than is required to drive a circular chart.
2. Observing behavior several hours or days back is not as easy as picking out one circular chart which covers the desired period of time

## Slide 47
11.7 Application of Strip Chart Recorder
Following are some of the important applications of Heterodyne Wave Analyser, which are important from the subject point of view :
In temperature recorder: A strip chart recorder may be used to provide a graphic record of temperature as a function of time.
There are two primary methods used for recording temperature:
(i) the thermocouple method and
(ii) the resistance method.

## Slide 48
2. Sound level recording: It is required to obtain a record of sound level over a period of time near hospitals, schools or residences, airports etc. It can be done with an ordinary microphone and a strip-chart recorder.
3. Recording amplifier drift: Transistor amplifiers are sensitive to temperature changes.
The changes in temperature cause the bias voltage of the transistor to change.
Due to this the operating or quiescent point of transistor is changed by small amount.
This change in the quiescent point is called drift. The drift is recorded by connecting the recorder to the output of the amplifier

## Slide 50: Galvanometer Type Recorder:
The D’Arsonval movement used in moving coil indicating instruments can also provide the movement in a Galvanometer Type Recorder.
The D’Arsonval movement consists of a moving coil placed in a strong magnetic field, as shown in Fig. 12.2(a).

## Slide 52
In a galvanometer type recorder, the pointer of the D’Arsonval movement is fitted with a pen-ink (stylus) mechanism.
The pointer deflects when current flows through the moving coil. The deflection of the pointer is directly proportional to the magnitude of the current flowing through the coil.
As the signal current flows through the coil, the magnetic field of the coil varies in intensity in accordance with the signal. The reaction of this field with the field of the permanent magnet causes the coil to change its angular position. As the position of the coil follows the variation of the signal current being recorded, the pen is accordingly deflected across the paper chart.

## Slide 53
The paper is pulled from a supply roll by a motor driven transport mechanism. Thus, as the paper moves past the pen and as the pen is deflected, the signal waveform is traced on the paper.
The recording pen is connected to an ink reservoir through a narrow bore tube. Gravity and capillary action establish a flow of ink from the reservoir through the tubing and into the hollow of the pen.
Galvanometer type recorders are well suited for low frequency ac inputs obtained from quantities varying slowly at frequencies of upto 100 c/s, or in special cases up to 1000 c/s.
Because of the compact nature of the galvanometer unit (or pen motor) this type of recorder is particularly suitable for multiple channel operation. Hence it finds extensive use in the simultaneous recording of a large number of varying transducers outputs.

## Slide 54
This recorder uses a curvilinear system of tracing. The time lines on the chart must be arcs of radius R (where R is the length of the pointer), and the galvanometer shaft must be located exactly at the center of curvature of a time line arc.
Improper positioning of the galvanometer or misalignment of the chart paper in the recorder can give a distorted response, i.e. having a negative rise time or a long rise time.
One method of avoiding the distorted appearance of recordings in curvilinear coordinates is to produce the recording in rectangular coordinates. In this design, the chart paper is pulled over a sharp edge that defines the locus of the point of contact between the paper and the recording stylus.
The stylus is rigidly attached to the galvanometer coil and wipes over the sharp edge as the coil rotates.

## Slide 55
In one of the recorders, the paper used is usually heat sensitive, and the stylus is equipped with a heated tip long enough to guarantee a hot point of contact with the paper, regardless of the stylus position on the chart. Alternatively the paper can be electrically sensitive, in which case the stylus tip would serve to carry current into the paper at the point of contact.
The recorders can work on ranges ranging from a few mA/mV to several mA/mV. These moving galvanometer type recorders are comparatively inexpensive instruments, having a narrow bandwidth of 0 — 10 Hz. They have a sensitivity of about 0.4 V/mm, or from a chart of 100 mm width a full scale deflection of 40 mV is obtained.
In most instruments, the speed of the paper through the recorder is determined by the gear ratio of the driving mechanism. If it is desired to change the speed of the paper, one or more gears must be changed.

## Slide 56
Paper speed is an important consideration for several reasons.
If the paper moves too slowly, the recorded signal variations are bunched up and difficult to read.
If the paper moves too fast, the recorded waveform will be so spread out that greater lengths of paper will be required to record the variations of the signal. It also makes the task of reading and interpreting the waveforms more difficult.
Also, the operator can determine the frequency components of the recorded waveform, if he knows how fast the paper has moved past the pen position. The paper is usually printed with coordinates, such as graph

## Slide 57
Some recorders contain a timing mechanism that prints a series of small dots along the edge of the paper chart, as the paper moves through the recorder. This time marker produces one mark per second.
These types of recorders are mostly used as optical recorders, and contain a light source provided by either an ultra violet or tungsten lamp.
A small mirror is connected to the galvanometer movement and the light beam is focussed on this mirror, as shown in Fig. 12.2(b).
The beam reflected from the mirror is focussed into a spot on a light sensitive paper.
As the current passes through the coil, the mirror deflects. The movement of the light beam is affected by the deflection of the small mirror, and the spot on the paper also varies for the same reason, thus tracing the waveform on the paper.

## Slide 58
Advantages
The galvanometer type strip chart recorder has a number of advantages.
Some of the important ones are given below:
The system is comparatively inexpensive.
2. It records very low frequency a.c. signals.
3. We can change the speed of paper as per requirement