## Slide 1: Module – 2 : Applications of Diodes
Chapter 1: Diodes and Applications
Reference: Robert L. Boylestad, Louis Nashelsky, Electronic Devices & Circuit Theory, 11th Edition, PHI, 2012
Part – I : Analog Electronics

## Slide 2: Application of Diodes
At the end of this module, students will be able to:
Explain need for AC to DC conversion
Discuss basic DC power supply unit.
Discuss and analyze the working of a various rectifier circuits.
Explain how capacitor filter can be used to minimize the ac component.

## Slide 3: INTRODUCTION
What is an AC and an DC signal?
Eg. of AC signal
Define
Average value
RMS or effective value
Electricity Distribution in INDIA: AC signal of 230V, 50HZ.
Necessity of DC power: Many electronic gadgets
Fig. 1: AC signal with A=230√2V, f=50Hz
Note: The average or DC value of this signal is equal to zero.
Notes: AC signal: Is a signal whose values keep changing, such that the average value is zero.
Figure: A=230x(root(2)) V, f=1/20msec=50Hz
DC signal: A signal that is constant valued.
Pure sinusoidal input signal Vin(t); A is the Amplitude in volts, w=2𝜋𝑓 called angular frequency in rad/sec, f is frequency in Hz.
Average or DC value: The dc value of a signal is the average value of that signal. The root mean square(RMS) value of the signal is the effective value which produces the same heating effect as the alternating component. Mathematical equations refer notes equation (1.2.1) & (1.2.2)
The average value of this signal is zero.

## Slide 4: INTRODUCTION
Fig. 2 : Block Diagram of Basic DC power supply
Notes: A step down transformer reduces the voltage of an ac signal is called a step down transformer.
Rectifiers converts an ac sinusoidal signal that is bidirectional with positive and negative amplitudes into a signal with only unidirectional amplitudes that is only positive or only negative. Thus rectifier circuit forces the current through the load to flow in only in one direction. The out put of rectifier is called pulsating dc signal.
Converts AC signal to pulsating DC
Primary element: Diode
Two types of rectifiers are: Half wave rectifier
Full wave rectifier
Full wave rectifier
  Center-tapped transformer FWR
  Bridge FWR
A filter circuit filters ac content from pulsating dc. A filter has to have a capacitor, an energy storing component that can hold the voltage to the peak value of the rectified pulsating dc and then dissipate energy to load when the pulsating dc drops.
Finally regulator is used to provide constant dc voltage despite of variations in the mains ac power supply or load variations.

## Slide 5: Activity
List in a table the names of at least six products/applications that we use in daily life that require dc power supply along with the range of values.
List the appliances or products around us that need power supply. Classify them under the umbrella of dc or ac power supply that is used for its working.
Notes: One cannot imagine life without electronic products like iron box, mixers, grinders, refrigerators, washing machines, microwave oven, televisions, mobiles, computers, laptops to name a few that we use in our daily lives. Some of them need AC power supply and some need DC power supply. First two test question is an activity just to know electronic equipment's that we use everyday better.
Next two test question is a summary of what we discussed so far and that we will be studying in detail in the following sections.

## Slide 6: CONTENT
Introduction: Basic DC power supply
Half wave rectifier (HWR)
Full wave rectifiers:
              Center tapped FWR
              Bridge Rectifier
Capacitor filter

## Slide 7: RECTIFIER
Converts AC signal to pulsating DC
Primary element: Diode
Two types of rectifiers are:
  Half wave rectifier
  Full wave rectifier
Full wave rectifier
  Center-tapped transformer FWR
  Bridge FWR
Notes:   HWR: Only half of the input cycle (positive or negative) is rectified
  FWR: Both positive and negative half cycles are rectified

## Slide 8: HALF WAVE RECTIFIER (HWR)
Diode passes only for half of the signal time period Hence the name HWR.
Fig 7: Circuit of HWR
Notes: The half wave rectifier consists of a single semiconductor diode, the key component of rectifiers.
Diode passes only for half of the signal time period and hence the name HWR.
The secondary voltage of transformer (node between A & B) is fed as an input of a rectifier circuit. The output is measured across the load resistor RL

## Slide 9: Working HWR
During Positive half Cycle of input signal
Equivalent Circuit of HWR, when node A is positive w.r.t node B
Notes: Fig 8: Voltage at node A is positive with respect to voltage at node B, forces the diode to be forward bias and act as a short. This results in current flow through the load resistance RL. Hence output voltage is approximately equal to the secondary voltage.
fig. 9: during the negative half cycle, the voltage at node A is negative with respect to node B that forces the diode in reverse biased and act as open circuit. This results in no current flow through the load

## Slide 10: HWR Working
During Negative half Cycle of input signal
Fig 9: Equivalent Circuit of HWR, when node A is negative w.r.t node B
Note: Current through load exist only for one half cycle
Notes: Fig 8: Voltage at node A is positive with respect to voltage at node B, forces the diode to be forward bias and act as a short. This results in current flow through the load resistance RL. Hence output voltage is approximately equal to the secondary voltage.
fig. 9: during the negative half cycle, the voltage at node A is negative with respect to node B that forces the diode in reverse biased and act as open circuit. This results in no current flow through the load

## Slide 11: HALF WAVE RECTIFIER
Fig 10: Input and rectified output with ideal diode
Fig 11: Secondary input and rectified output with practical diode
Notes: Fig 10: diodes considered are ideal
Fig 11: Simulated result considering practical diode

## Slide 12: HALF WAVE RECTIFIER
Performance of Rectifiers is measured using the following parameters:
  DC voltage Vdc
  Peak Inverse Voltage (PIV)
  Ripple factor γ
  Efficiency η
Notes: PIV: It is defined as the maximum voltage across the reverse biased diode before the diode breaks down. It is essential that the diode used in rectifier circuit should be able to withstand the voltage available across it when it is reversed biased so that it acts as open circuit and does not enter into a breakdown state.
Ripple factor γ is defined as the ratio of rms value of ac component to dc component.
Ripple factor actually measures the amount of ac content still remaining as compared to the dc (or average) content in the pulsating dc.
Efficiency (η) is the ratio of the dc output power to ac input power
Efficiency signifies the outcome of the rectifier circuit to output dc power in comparison to ac input power.

## Slide 13: HALF WAVE RECTIFIER
During positive cycle
    i = Im sin(ωt)
    Peak current
    Assume ideal diodes
During negative half cycle,
i = 0

## Slide 14: HALF WAVE RECTIFIER
Average (DC) current
Average output voltage is
Average value of load current in half wave rectifier is non zero

## Slide 15: HALF WAVE RECTIFIER
RMS value of load current in half wave rectifier is:
RMS output voltage is

## Slide 16: HALF WAVE RECTIFIER
PIV : should be greater than Vm , peak of secondary voltage.
Ripple factor is:
Efficiency:

## Slide 17: HALF WAVE RECTIFIER
Self Test
HWR is used to rectify the AC signal which has peak value of 25V. Which all diodes can be selected whose PIV rating is
(a) 5V (b) 15V (c) 30V (d) both a and b
what happens when the diode connection is reversed? Draw the input and output waveform. Will the values of PIV, ripple factor and efficiency for this changed circuit change?

## Slide 18: HALF WAVE RECTIFIER
Advantages of HWR
  Simple circuit
  Single diode
  PIV rating is Vm
Disadvantages of HWR
  High ripple factor
  Low efficiency

## Slide 19: Center Tapped FWR
Fig.12 center tapped FWR
Fig. 13: Secondary waveforms
Notes: The output of a center tapped transformer is available in three different forms. The secondary voltage observed between the extreme end nodes i.e between node A and node B is a stepped down voltage as shown in fig. 13(a). The voltages measured at between node A and center node (ground) or node B and center node is half in magnitude in comparison to the voltage measured between node A and node B. Also very interesting point is that voltage at node A is 180° out of phase with the voltage at node B when measured relative to the center node (ground). All these secondary waveforms are shown in fig. 13b,c

## Slide 20: Working of center tapped FWR
Fig. 14: Center tapped FWR for node A is positive w.r.t B
Fig. 15: Center tapped FWR for node B is positive w.r.t. A
Note: Current through load during both cycles is in same direction (from node C to ground)
Notes: During the first half cycle, the voltage at node A is positive and voltage at node B is negative measured with respect to ground. Diode D1 gets forward biased and acts as a short whereas diode D2 is reverse biased and acts as open. This results in a current flow through upper half secondary windings of transformer, diode D1 and the load RL. Direction of the current through the load is towards the ground from node C. Hence the output voltage measured at node C with respect to ground is equal to voltage at node A measured with respect to ground.
Similar explaination holds good for second half of time period

## Slide 21: Center Tapped FWR
Fig. 16 : Input secondary and output waveforms
Note: The frequency of the output signal =2 times the input frequency
Notes: The output waveform observed across load resistor along with voltage waveforms at node A and node B with respect to ground
Thus rectified output is unidirectional that exist for the entire time period.
Also

## Slide 22: Center tapped FWR
The Average of output voltage
RMS value of the voltage at the load is
The Average of output current

## Slide 23: Center tapped FWR
PIV : 2Vm , where Vm peak of secondary voltage (between node A and ground or between node B and ground)
Ripple factor is:
Efficiency:

## Slide 24: Solved Exercise
A center-tapped FWR is supplied with 230V, 50 Hz AC mains through a step down transformer with turns ratio equal to 10. Find the average and RMS value of the load current, rating of the diode used for proper working. PIV .
Given: Input AC mains RMS voltage =230V, turns ratio=10,
  Hence Secondary RMS voltage =230/10=23V
Solution: ….

## Slide 25: Center Tapped FWR
Choose the correct answer: (T is the time period of the input signal)
In HWR, the diode is forward biased for what duration of the time period?
(a) T/2 b) T/4 c) 3T/4 d) T
In center tapped FWR, each diode is forward biased for what duration of the time period?
(a) T/2 b) T/4 c) 3T/4 d) T
In a center tapped FWR , current through load resistor flows for what duration of the time period?
(a)T/2 b) T/4 c) 3T/4 d) T
The ripple factor of FWR is greater than HWR
(a) True (b) False
Notes: Ans: 1. T/2 2. T/2 3. T

## Slide 26: Comparison of HWR and FWR
Advantages of center tapped FWR over HWR
  High Efficiency
  low ripple factor
Disadvantages of center tapped FWR over HWR
  Uses 2 diodes
  Uses center tapped transformer

## Slide 27: Bridge rectifier
Notes: The bridge rectifier consists of four diodes in the form of a bridge. We can represent two parallel paths, each path with two diodes and all diodes directed in the same direction. The top path consists of diode D3 and D1 whereas bottom path consists of diode D2 and D4 respectively. Load resistor is connected between the ends of two parallel paths (i.e node C and ground). The secondary input is between the two centers of two the two parallel paths (one between D1,D3 and other between D4, D2)
Output is measured across load resistor.

## Slide 28: Working of Bridge FWR
Fig. 18: Bridge FWR when node A is positive w.r.t B
Fig. 19: Bridge FWR when node B is positive w.r.t. A
Note: Current through load for both cycles is in same direction (from node C to ground)
Notes: For the first half of the time period, during which node A is positive with respect to B, D1 and D2 are forward biased whereas D3 and D4 are reverse biased. As said earlier considering ideal diodes D1, D2 are shorted and D3,D4 are open as in fig 18. This results in a current flow taking a closed path from node A, through D1, R-Load, D2 and from node B through the secondary coil as indicated. Note that current through the load resistor flows from node C to ground.
Similarly for the second half of the time period, during which node B is positive with respect to A, D3 and D4 are forward biased whereas D1 and D2 are reverse biased. Diodes D3, D4 are shorted and D1,D2 are open as shown in figure 19. This results in a current flow taking a closed path from node B, through D4, R-Load, D3 and from node A through the secondary coil as indicated. Note that again current through the load resistor flows from node C to ground even though the current through the secondary has reversed.
Thus output voltage is unidirectional for both the half cycle

## Slide 29: Bridge FWR
Fig. 20 : Input and output waveforms of bridge rectifier
Note: The frequency of the output signal =2 times the input frequency

## Slide 30: Bridge FWR
PIV : Vm , where Vm peak of secondary voltage (between node A and node B).
Other parameters same as Center tapped FWR:
Ripple factor is:
Efficiency:

## Slide 31: Comparison of Rectifiers
Parameters of rectified signal | HWR | Center-tapped FWR | Bridge FWR
Vdc |  |  | 
VRMS |  |  | 
PIV |  |  | 
Ripple factor |  |  | 
Efficiency |  |  | 
Frequency fo |  |  | 
1.21 0.483 0.483
40.6% 81.2% 81.2%

## Slide 32: Capacitor Filter
Commonly referred as C type filter
Key component of filter is the energy storing elements. Example: Capacitor
Capacitor helps to hold the output voltage to its maximum or peak value.
It can be used with HWR as well as with FWR

## Slide 33: Capacitor Filter
Fig 21: C type filter with HWR
Notes: The property of a capacitor is that, it allows ac component and blocks dc component. The operation of the capacitor filter is to minimize the ripple and to increase the dc voltage.

## Slide 34: Capacitor Filter
Notes: The property of a capacitor is that, it allows ac component and blocks dc component. The operation of the capacitor filter is to minimize the ripple and to increase the dc voltage.

## Slide 35: Capacitor Filter
Fig 22: C type filter with Bridge FWR
Notes: The property of a capacitor is that, it allows ac component and blocks dc component. The operation of the capacitor filter is to minimize the ripple and to increase the dc voltage.

## Slide 36: Capacitor Filter
Notes: The property of a capacitor is that, it allows ac component and blocks dc component. The operation of the capacitor filter is to minimize the ripple and to increase the dc voltage.

## Slide 37: Capacitor Filter
Fig. 23 Filtered output waveform using C type filter
Notes: The property of a capacitor is that, it allows ac component and blocks dc component. The operation of the capacitor filter is to minimize the ripple and to increase the dc voltage.

## Slide 38: Ripple factor with Capacitor Filter
For HWR
For FWR

## Slide 39: Output DC Voltage with Capacitor Filter
DC value of filtered output for HWR
Note: here f is the frequency of the input signal
DC value of filtered output for FWR

## Slide 40: Comparison of Rectifiers
Parameters of rectified signal | HWR | FWR
Vdc |  | 
Ripple factor |  | 

## Slide 41: Summary
At the end of this module, students will be able to:
Discuss block diagram of a basic DC power supply unit.
Explain and analyze the working of various rectifier circuits.
Evaluate Output DC value, ripple factor, efficiency and PIV, of different rectifier circuits.
Explain the working of rectifier circuits with capacitor filter

## Slide 42: Exercise Problems
  Primary voltage is 120V, 60Hz. Turns ratio is 5:1. This transformer supplies to bridge rectifier employing 4 identical ideal diodes. The load resistance is 1kΩ. Calculate average and rms load voltage, efficiency, ripple factor, PIV rating and frequency of output waveform.
  Repeat this problem for center tapped FWR. Comment on the results comparing with results of exercise 1.

## Slide 43: Exercise Problems
  A half wave rectifier with capacitor filter is supplied from transformer having peak secondary voltage 20V and freq 50Hz. The load resistance is 560Ω and capacitor used is 1000μF. Calculate ripple factor and dc output voltage. Draw the filtered output and label peak and dc value.
  (Ans. for part a: 0.0103, 19.65V)