## Slide 1: Part – I : Analog Electronics
Chapter-2: BJT and its Applications
Reference:
Robert L. Boylestad, Louis Nashelsky, Electronic Devices & Circuit Theory, 11th Edition, PHI, 2012
MODULE 1: BJT Characteristics

## Slide 2: BIPOLAR JUNCTION TRANSISTOR
Objectives
Discuss the operation of BJT.
Draw CB and CE configuration of transistor.
Explain input and output characteristics of CB and CE Configurations of transistor.
Derive expressions for current gains in transistor.

## Slide 3: INTRODUCTION
IMAGES OF TRANSISTOR
( Courtesy : wikipedia.org )
Notes: Invented by a team of scientists at Bell laboratories during 1947-48.
Advantages of Transistors
  Small size and light weight
  Low power consumption and operating voltages
  Low price

## Slide 4: INTRODUCTION
BJT has two junctions – Emitter-Base (EB) Junction and Collector-Base (CB) Junction.
Two types of transistors: NPN and PNP
Notes: The device is called “bipolar junction transistor” because current is due to motion of two types of charge carriers – free electrons & holes.

## Slide 5: INTRODUCTION
The three layers of BJT are called Emitter, Base and Collector
Base is lightly doped. Emitter is heavily doped. Collector is moderately doped
NPN – Emitter and Collector are N-type
semiconductors, Base is P-type
PNP – Emitter and Collector are P-type
semiconductors, Base is N-type
Notes: The width of emitter is more compared to collector region but less compared to base region.

## Slide 6: INTRODUCTION
Transistor symbols:
NPN Transistor PNP Transistor

## Slide 7: NPN TRANSISTOR OPERATION
http://www.learnabout-electronics.org/bipolar_junction_transistors_05.php
Notes: Operation of PNP is similar with roles of free electrons and holes interchanged.

## Slide 8: NPN TRANSISTOR OPERATION
Notes: Operation of PNP is similar with roles of free electrons and holes interchanged.

## Slide 9: NPN TRANSISTOR OPERATION
Notes: Operation of PNP is similar with roles of free electrons and holes interchanged.

## Slide 10: NPN TRANSISTOR OPERATION
Notes: Operation of PNP is similar with roles of free electrons and holes interchanged.

## Slide 11: CURRENTS IN TRANSISTOR
For both NPN and PNP transistor:
Collector current:
  : Current due to injected charge carriers from
  emitter
  : Current due to thermally generated minority
  carriers
Neglecting reverse saturation current ICBO ,
αdc : Common-base dc current gain
Notes: Value of αdc < 1, since IE>IC

## Slide 12: CURRENTS IN TRANSISTOR
βdc : Common emitter dc current gain
link\CURRENT RELATION.docx
  Reverse saturation current in CE configuration
    Note ICEO >> ICBO
Notes: Β>1, since IB < IC

## Slide 13: TRANSISTOR CONFIGURATIONS
BJT has three terminals
Accordingly three configurations exist:
  Common Base (CB) configuration
  Common Emitter (CE) configuration
  Common Collector (CC) configuration
    (The last one is not discussed in this course)

## Slide 14: COMMON BASE CONFIGURATION
Base is common between input and output terminals

## Slide 15: CB CONFIGURATION INPUT CHARACTERISTICS
CB Input characteristics
  A plot of IE versus VEB for various values of VCB.
  link\CB CHARACTERISTICS.docx

## Slide 16: CB CONFIGURATION OUTPUT CHARACTERISTICS
  A plot of IC versus VCB for various values of IE .
    Divided into three regions:
      Active Region
      Saturation Region
      Cutoff Region
link\CB CHARACTERISTICS.docx
Notes: Active region: E-B junction is forward biased and C-B junction is reverse biased.
Saturation region: E-B junction forward biased and C-B junction is forward biased.
Cut-off region: E-B junction is reverse biased and C-B junction is reverse biased.

## Slide 17: COMMON EMITTER CONFIGURATION
Emitter is common between input and output terminals

## Slide 18: CE CONFIGURATION INPUT CHARACTERISTICS
Plot of IB versus VBE for
various values of VCE
link\CE Characteristics.docx

## Slide 19: CE CONFIGURATION OUTPUT CHARACTERISTICS
  A plot of IC versus VCE for various values of IB .
    Divided into three regions:
      Active Region
      Saturation Region
      Cutoff Region
link\CE Characteristics.docx

## Slide 20: Exercise Problems
An NPN transistor has collector current 4mA and base current 10 μA. Calculate the alpha and beta values of the transistor, neglecting the reverse saturation current ICBO.
(Ans: 0.9975, 400)
In a transistor, 99% of the carriers injected into the base cross over to the collector region. If collector current is 4mA and collector leakage current is 6 μA, Calculate emitter and base currents. (Ans: 4.034 mA, 34μA)
In a transistor circuit, when the base current is increased from 0.32 mA to 0.48 mA, the emitter current increases from 15 mA to 20 mA. Find αac and βac values. (Ans: 0.968, 30.25)

## Slide 21: Summary
In this module we have learnt:
The operation of a transistor and the relevant current components.
To plot the input and output characteristics of CB and CE Configuration transistor.
To find current gains in different configurations of transistor.

## Slide 22: Part – I : Analog Electronics
Chapter-2: BJT and its Applications
Module 2: Transistor Biasing
Reference:
Robert L. Boylestad, Louis Nashelsky, Electronic Devices & Circuit Theory, 11th Edition, PHI, 2012

## Slide 23: Module 2: Transistor Biasing
Department of Electronics and Communication Engineering, MIT, Manipal
2
Objectives
Discuss the concept of biasing of the transistor.
Analyse the fixed and self bias circuits.
Identify the circuit parameters that effect Q point.

## Slide 24: Biasing
Applying external dc voltages to ensure that transistor operates in the desired region.
Transistor circuit in CE Configuration
Applying KVL collector loop
Coordinates of load line
VCE =VCC ; IC = 0 mA
VCE =0 ; IC = VCC/RC

## Slide 25: Load line and Operating point
Notes: Operating Point: Intersection of load line with the base current results in operating point or Q point.

## Slide 26: Load line and Operating point
Variation in load
line with circuit
parameters VCC,
RC and RB

## Slide 27: Types of Biasing
Two types
  Fixed bias
  Voltage divider bias (self bias)

## Slide 28: Transistor biasing
Department of Electronics and Communication Engineering, MIT, Manipal
2
  Fixed bias
  link\fixed bias.docx
Notes:   The value of IB is “fixed” by choosing proper value for RB.

## Slide 29: Exercise Problems
Department of Electronics and Communication Engineering, MIT, Manipal
2
A Si transistor is biased for a constant base current. If β = 80, VCEQ = 8 V, RC = 3 kΩ and VCC = 15 V, find ICQ and the value of RB required. ( Ans: 2.33mA, 493KΩ)
Repeat the above problem , if the transistor is a Germanium device. ( Ans: 2.33mA, 507KΩ)

## Slide 30: Transistor Biasing
Department of Electronics and Communication Engineering, MIT, Manipal
2
  2. Voltage divider bias (self bias)
Notes:   --Voltage-divider resistors R1 & R2 replace RB. of fixed bias.

## Slide 32: Transistor Biasing
Department of Electronics and Communication Engineering, MIT, Manipal
2
Equivalent circuit :
link\self bias.docx
Notes: Since IC is almost independent of β, Q-point is stable

## Slide 34: Exercise Problems
Department of Electronics and Communication Engineering, MIT, Manipal
2
For a self-bias circuit using silicon transistor, RE = 300 Ω, RC = 500 Ω, VCC = 15 V, β = 100 and β RE = 10R2. Find the values of R1 and R2 to get VCEQ = VCC / 2.
(Ans: 9.03KΩ)
For a self-bias circuit, the transistor is a Si device, RE = 200 Ω, R1 = 10R2 = 10 kΩ, RC = 2 kΩ, β = 100 and VCC = 15 V. Determine the values of ICQ and VCEQ.
( Ans: 3.13mA, 8.11V)

## Slide 35: Summary
In this module we have learnt:
Importance of biasing in transistors
Concept of load line, operating point and their significance
Operating point dependent on the circuit parameters such as supply voltage and resistor values as well as operating temperatures.
To analyse fixed bias circuit to obtain the operating point and plot the load line.
Finding the equivalent circuit for self bias circuit and analyse it to obtain the Q point.

## Slide 36: Part – I : Analog Electronics
Chapter-2: BJT and its Applications
Module 3: Transistor as an Amplifier
Reference:
Robert L. Boylestad, Louis Nashelsky, Electronic Devices & Circuit Theory, 11th Edition, PHI, 2012

## Slide 37: Module-3 : Transistor as an Amplifier
Objectives
Discuss the basic concepts of an amplifier.
Analyze the RC coupled amplifier circuit with and without feedback.
Plot the frequency response of an amplifier and define the bandwidth.

## Slide 38: Transistor Amplifier
Department of Electronics and Communication Engineering, MIT, Manipal
2
Collector current
Output voltage
Vout = Vcc-iCRc
Voltage gain ,
AV= Vout /Vin .
link\amplifier.docx
Notes: Amplifier: Device which gives larger swing in output voltage proportional to the input voltage swing.
Biasing the circuit fixes the operating point in the middle of active region required for faithful amplification.
current direction through RL is from bottom to top, the output voltage is 180o out of phase with input.

## Slide 39: Transistor Amplifier
Department of Electronics and Communication Engineering, MIT, Manipal
2
Input and output waveforms of amplifier
Notes: Gain dependent on β, RC and other physical parameters of the transistor.
There is a dc shift in the output voltage waveform.
Output voltage is 180o out of phase with input voltage.

## Slide 40: Transistor Amplifier
Department of Electronics and Communication Engineering, MIT, Manipal
2
RC Coupling
link\RC coupling.docx
Notes: CC is coupling capacitor (to block dc ), CE is emitter bypass capacitor (to prevent feedback).
R1 ,R2, ,RE ,RC are used for biasing

## Slide 41: Transistor Amplifier
Department of Electronics and Communication Engineering, MIT, Manipal
2
  Frequency response of amplifier:
  Bandwidth of amplifier : fH - fL.
  link\freqency response.docx
Notes:     Frequency response is a plot of gain versus frequency.
    3 dB frequency: The frequency were gain reduced by 3 dB of its maximum value.

## Slide 42: Transistor Amplifier
Department of Electronics and Communication Engineering, MIT, Manipal
2
  Frequency response of amplifier:
  Bandwidth of amplifier : fH - fL.
  link\freqency response.docx
Notes:     Frequency response is a plot of gain versus frequency.
    3 dB frequency: The frequency were gain reduced by 3 dB of its maximum value.

## Slide 43: Transistor Amplifier
Department of Electronics and Communication Engineering, MIT, Manipal
2
Effect of biasing in an amplifier.

## Slide 44: Transistor Amplifier application
Department of Electronics and Communication Engineering, MIT, Manipal
2
.
Source: www.sentex.ca

## Slide 45: Multistage Amplifier
Department of Electronics and Communication Engineering, MIT, Manipal
2
Gain in decibels,
(AV)dB = 20 log10 | AV |
Multistage transistor
Notes: Up to gain of 100 (i.e., 40 dB) is obtained with single transistor.
For larger gain, more amplifier stages are to be cascaded.

## Slide 46: Summary
In this module we have learnt:
Amplifier circuits are used for increasing the strength of week signal.
The working of an RC coupled amplifier with and without feedback.
The Gain of the amplifier defined as ratio of output signal to input signal.
The frequency response is a plot of frequency v/s gain of the amplifier and defines the bandwidth.
Gain of multistage amplifiers will be obtained by multiplying gain of each individual stage.

## Slide 47: Part – I : Analog Electronics
Chapter-2: BJT and its Applications
Module 4: Transistor as a Switch
Reference:
Robert L. Boylestad, Louis Nashelsky, Electronic Devices & Circuit Theory, 11th Edition, PHI, 2012

## Slide 48: Module 4: Transistor as Switch
Objectives
Explain the use of transistor as switch.
Application of transistor switch as LED driver and Inverter.

## Slide 49: Transistor as switch
Transistor operate as “ON/OFF” type switch.
link\switch.docx
Notes: When Input voltage VIN is ZERO , transistor is OFF(cut-off region), Vout = VCC.
When Input voltage VIN is HIGH , transistor is ON (saturation region) , Vout = 0.

## Slide 50: Transistor as LED driver
Department of Electronics and Communication Engineering, MIT, Manipal
2
Notes: When Input voltage VIN is ZERO , transistor is OFF(cut-off region), LED is OFF..
When Input voltage VIN is HIGH , transistor is ON (saturation region) , LED turns ON.

## Slide 51: Transistor as Inverter
Notes: When A = 0 , transistor is OFF(cut-off region), Output Q = 1.
When A = 1, transistor is ON (saturation region) , Output Q = 0.

## Slide 52: Summary
In this module we have learnt:
The transistor can be used as switch by operating it in either saturation region (when the switch is said to be ON) or in cut off region (when the switch is said to be OFF).
The applications of transistor switch as LED driver and inverter.