## Slide 1: THUMB IMPLEMENTATION

## Slide 2
The Thumb instruction set addresses the issue of code density.
It may be viewed as a compressed form of a subset of the ARM instruction set.
Thumb instructions map onto ARM instructions, and the Thumb programmer's model maps onto the ARM programmer's model.
If T bit in CPSR is set the processor interprets the instruction stream as 16-bit Thumb instructions, otherwise it interprets it as standard ARM instructions.

## Slide 3: THUMB ENTRY
ARM cores start up, after reset, executing ARM instructions.
The normal way they switch to execute Thumb instructions is by executing a Branch and Exchange (BX) instruction.
This instruction sets the T bit if the bottom bit of the specified register was set, and switches the program counter to the address given in the remainder of the register.

## Slide 4: THUMB EXIT
An explicit switch back to an ARM instruction stream can be caused by executing a Thumb BX instruction.
An implicit return to an ARM instruction stream takes place whenever an exception is taken. (An exception entry is always handled in ARM)

## Slide 5: The Thumb programmer's model

## Slide 6
The Thumb instruction set is a subset of the ARM instruction set and the instructions operate on a restricted view of the ARM registers.
The instruction set gives full access to the eight 'Lo' general purpose registers r0 to r7, and makes extensive use of r13 to r15 for special purposes:
r13 is used as a stack pointer.
r14 is used as the link register.
r15 is the program counter (PC).
The remaining registers (r8 to r12 and the CPSR) have only restricted access.

## Slide 7: Thumb-ARM similarities
All Thumb instructions are 16 bits long. They map onto ARM instructions so they inherit many properties of the ARM instruction set.
The load-store architecture with data processing, data transfer and control flow instructions.
Support for 8-bit byte, 16-bit half-word and 32-bit word data types where half-words are aligned on 2-byte boundaries and words are aligned on 4-byte boundaries.
A 32-bit unsegmented memory.

## Slide 8: Thumb-ARM differences
Most Thumb instructions are executed unconditionally.
(All ARM instructions are executed conditionally.)
Many Thumb data processing instructions use a 2-address format (the destination register is the same as one of the source registers).
(ARM data processing instructions, with the exception of the 64-bit multiplies, use a 3-address format.)
Thumb instruction formats are less regular than ARM instruction formats, as a result of the dense encoding.