## Slide 1: GPIO

## Slide 2: Applications of GPIO
General purpose I/O
  • Driving LEDs, or other indicators
  • Controlling off-chip devices
  • Sensing digital inputs

## Slide 3
When getting started in embedded programming, GPIO (viz. General Purpose Input Output) pins are important.
The use of GPIO is not limited to driving LEDS but can be also used for reading digital signal , generating triggers for external components , controlling external devices etc….

## Slide 4
Most of the function oriented pins on lpc214x Microcontrollers are grouped into ports. lpc2148 has 2 ports viz. Port 0 and Port 1.
Port 0 is a 32 bit wide I/O port (i.e it can be used for max 32 pins where each pin refers to a corresponding bit) and has dedicated direction bits for each of the pins present in the port. 28 out of the 32 pins can be used as bi-directional I/O (digital) pins. Pins P0.24 , P0.26 & P0.27 are unavailable for use and Pin P0.30 can be used as output pin only.
Port 1 is also a 32 bit wide I/0 port but Pins 0 to 15 i.e P1.0 – P1.15 are unavailable for use and this port too has a dedicated direction bit for each of the usable pins.

## Slide 5: Pin connect block
Allows individual pin configuration.
The purpose of the Pin connect block is to configure the microcontroller pins to the desired functions.
In lpc214x MCUs most of the PINS are Multiplexed i.e. these pins can be configured to provide different functions.
The functions of the Pins in Port 0 & 1 can be selected by manipulating appropriate bits in PINSEL0/1/2 registers.
assigning ’0′ to these registers forces the corresponding pins to be used as GPIO

## Slide 6
Since by default all pins are configured as GPIOs we dont need to explicitly assign zero value to PINSELx registers in GPIO programming.
The purpose of the Pin Connect Block is to configure the microcontroller pins to the desired functions. The pin connect block allows selected pins of the microcontroller to have more than one function.

## Slide 7
Two bits from PINSEL register will be used to select the multi functions of the pins.
PINSEL0: P0.0-P0.15
PINSEL1: P0.16-P0.31
PINSEL2: P1.16-P1.31

## Slide 8: Registers in GPIO Programming
1. IOxPIN (x=port number) (32 bit) : Pin value register-Regardless of the direction set for the particular pins it gives the current status of the GPIO pin when read.
2. IOxDIR (32 bit) : This is the GPIO direction control register. Setting a bit to 0 in this register will configure the corresponding pin to be used as an Input while setting it to 1 will configure it as Output.
3. IOxSET (32 bit) : This register controls the state of output pins. This register can be used to drive an ‘output’ configured pin to Logic 1 i.e HIGH. Writing Zero does NOT have any effect and hence it cannot be used to drive a pin to Logic 0 i.e LOW. For driving pins LOW IOxCLR is used. 4. IOxCLR (32 bit) : This register can be used to drive an ‘output’ configured pin to Logic 0 i.e LOW. It cannot be used to drive a pin to Logic 1. Writing ones produces lows at the corresponding port pins and clears the corresponding bits in the IOSET register.

## Slide 9: Example-sequential accesses to IOSET and IOCLR affecting the same GPIO pin/bit
IO0DIR = 0x0000 0080 ;pin P0.7 configured as output
IO0CLR = 0x0000 0080 ;P0.7 goes LOW
IO0SET = 0x0000 0080 ;P0.7 goes HIGH
pin P0.7 is configured as an output (write to IO0DIR register). After this, P0.7 output is set to low (first write to IO0CLR register). Short high pulse follows on P0.7 (write access to IO0SET), and the final write to IO0CLR register sets pin P0.7 back to low level.

## Slide 10: Example to generate square waveform at P0.0-P0.3
# include <lpc214x.h>
Int main (void)
{
unsigned int x;
for(;;)
{
IO0DIR=0xFFFFFFFF;
for (x=0;x<4;x++)
IO0SET=0x0000000F;
for (x=0;x<12;x++)
IO0CLR=0x0000000F;
}
}

## Slide 11: 50% duty cycle on P0.16
# include <lpc214x.h>
Int main (void)
{
unsigned int x;
IO0DIR=0x00010000;
while(1)
{
IO0SET=1<<16;
  delay ();
  IO0CLR=1<<16;
  delay();
}
}

## Slide 12
void delay(void) { int z, c; c=0; for(z=0; z<4000000; z++) // You can edit this as per your needs { c++;
} }