## Slide 1: Basic Electrical Technology [ELE 1051]
L26 - Electrical Power system components & Transformers

## Slide 2: Outline
Power System Components
  Generation
  Transmission, Distribution
  Protection & Control
Types of Loads

## Slide 3: Power System Background
Branch of Electrical Sciences dealing with Generation, Transmission & Distribution of electrical energy.
Pearl Street Station in New York City, 1882
  “Illuminating Companies” by Thomas A Edison
  Concept of DC power generation
Three phase AC power system,1896
  2 generators and a transmission line @ 25 Hz.

## Slide 4: Power System Structure
Courtesy: Olle I Elgerd

## Slide 5: Power System Components
Generation subsystem
Transmission subsystem
Sub-transmission subsystem
Distribution subsystem
Protection and Control subsystem

## Slide 6: Generation Subsystem
Primary Sources of Energy
  Fossil Fuel
    Coal, Oil, Natural Gas
  Renewable Energy
    Water, Solar, Wind, Tidal, Geo-thermal etc.
  Nuclear Energy

## Slide 7: Generation Subsystem
Coal Fired Power plant
UPCL, Padubidri, Mangalore

## Slide 8: Generation Subsystem
Thermal Power Stations
  Coal Fired
    Turbo alternators driven by steam turbine
  Oil Fired
    Crude oil or Residual oil
  Gas Fired
    Combined cycle- First stage: Gas turbine, Second stage: Steam Turbine
  Diesel Fired
    Internal Combustion engines as prime mover
    Standby power plants

## Slide 9: Generation Subsystem
Hydroelectric Power Station
  Salient Pole alternators driven by turbines.
  Turbines: Impulse Turbine & Reaction Turbine
  Pumped storage plants
Varahi Power Plant, Udupi Dist.

## Slide 10: Generation Subsystem
Nuclear Power Plant
  Fissile Material
  Moderator
    D2O, Graphite
    Control rods
    Boron OR Cadmium
  Fast Breeder Reactors
    Liquid metal (alloy of Na & K) is coolant

## Slide 11: Generation Subsystem
Non-Conventional Power Stations
  Wind Power Stations
  Solar Power Stations
  Micro-Hydel Power Stations
  Bio-Mass Power Stations
  Geothermal Power Stations
Wind Farm in Karnataka
Solar Park, Charanka Village, Gujarat
1MW hydro plant, HP
Bio-mass Plant, Chattisgarh

## Slide 12: Transmission, Sub-transmission & Distribution Subsystems
Transmission networks- EHV AC or HVDC
  Operates @765 kV/400 kV/ 220 kV AC or  500 kV DC.
AC Sub-Transmission networks
  Operates @ 132 kV/ 110kV/ 66 kV/ 33 kV
AC Distribution Network
  Primary side: 11 kV
  Secondary side: 415 V, 4 Wire

## Slide 13: Share of Renewable resources in India
Resource | Potential (MW) | Upto 9th Plan | Upto 10th Plan | 11th Plan Target | Upto 30.09.10 | Cumulative Achievement | 12th Plan Projection (2017) | 13th Plan Projection (2022)
Wind Power | 48,500 | 1,667 | 5,427 | 9,000 | 4,714 | 12,809 | 27,300 | 38,500
Small Hydro Power | 15,000 | 1,438 | 538 | 1,400 | 759 | 2,823 | 5,000 | 6,600
Bio Power | 23,700 | 390 | 795 | 1,780 | 1,079 | 2,505 | 5,100 | 7,300
Solar Power | 20-30 MW/sq km | 2 | 1 | 50 | 8 | 18 | 4,000 | 20,000
Total |  | 3,497 | 6,761 | 12,230 | 6,560 | 18,155 | 41,400 | 72,400
Source: Ministry of New & Renewable Energy, Govt. of India

## Slide 14: Transmission Network – A Glance

## Slide 15: Substation
Substation Components
  Lightning Arrester
  Carrier line communication equipment (Wave Trap)
  Instrument Transformers (CT, PT)
  Circuit Breakers
  Isolators
  Bus Bars
  Power Transformers
  Control Room

## Slide 16: Protection & Control Subsystem
Fail free power is Hypothetical.
Faults: Open Circuit & Short Circuit
Faults detection : Relays.
Fault Isolation: Circuit Breakers
Modern Trend: Supervisory Control And Data Acquisition (SCADA) systems.

## Slide 17: Types of Loads
Industrial Loads
  3 Phase
  Complex Tariff Structure
Domestic Loads/Commercial Loads
  1 Phase
  Tariff based on energy consumed- kWH

## Slide 18: Domestic Loads and Power Ratings
Incandescent lamps - (5 W to 100 W)
Fluorescent lamps - (20 W & 40 W); CFL - (5 W to 25 W)
LED Lamps-(1W to 100W)
Air Conditioner (1.5 T) - 1800 W
Electric Iron - 750 W
Heaters/ Geysers – 2000 W
Ceiling Fan – 60 W
Washing Machine (with heater) – 2.5 kW
Refrigerator – 160 W
PC – 200 W, Laptop – 40 W
  Reduce Electricity bill by minimizing the use of heating / environmental conditioning gadgets

## Slide 19: Indian Power Sector – A Glance
Sector | MW | Percentage
State | 1,03617 | 27.7
Central | 93,927 | 25.1
Private | 1,76,655 | 47.2
Total | 3,74,199 | 100.0
As on 17/12/2020
Source: Ministry of Power, Govt. of India

## Slide 20: Indian Power Sector - A Glance
Fuel | MW | Percentage
Total Thermal | 2,31,321 | 61.8
Coal | 1,99,595 | 53.3
Lignite | 6,260 | 1.7
Gas | 24,957 | 6.7
Oil | 510 | 0.1
Hydro (Renewable) | 45699 | 12.2
Nuclear | 6,780 | 1.8
RES*(MNRE) | 90,399 | 24.2
Total | 3,74,199 | 100
*RES include small hydro, bio-mass, urban and industrial waste power and wind energy
As on 17/12/2020
Source: Ministry of Power, Govt. of India

## Slide 21: Summary
Detailed discussion of various power generating sources.
Different levels of voltages at transmission, sub-transmission and distribution stage.
Types of loads.
Indian Power Sector

## Slide 22: Basic Electrical Technology [ELE 1051]
L26 – Transformers

## Slide 23: Contents
Introduction
Operation
Representation
Emf Equation
Construction
  Core Type
  Shell Type
Losses & Efficiency
Auto Transformer
3 Phase Transformer
Applications

## Slide 24: Introduction
Static device with AC excitation
Transfers energy between two or more magnetically coupled circuits without change in frequency.
Principle of operation: Electromagnetic Induction
Electric circuits are linked by a common ferromagnetic core.
Ferromagnetic core ensures maximum magnetic flux linkage
Applications:
  Electric power systems.
    Power transmission, distribution networks.
  Electronic circuits.
  Electric traction.
Types |  | 
Based on Construction | Based on Function | Based on Windings
Core Type | Step Up | Single Winding
Shell Type | Step Down | 2 or 3 Windings
Notes: Picture Courtesy: Wikipedia

## Slide 27: Operation of Transformer
I1
E1
E2
V2
I2
LOAD
V1
Ø
Magnetic Core : Flux path
Flux Linkages : Primary & Secondary
Induced Emf :
  Primary – Self Induced Emf
  Secondary – Mutually Induced Emf

## Slide 28: Representation
Primary Side
Secondary Side
Core
V1
Supply Side
V2
Load Side
N1
N1 = Number of turns on primary
N2 = Number of turns on secondary
N2

## Slide 30: Emf Equation of Transformer

## Slide 31: Emf Equation of Ideal Transformer…
N2 > N1: Step Up
N1
N2
V1
V2
E2 > E1
V2 > V1 I1 > I2
N2 < N1: Step down
V1
V2
E2 < E1
V2 < V1
I1 < I2
N1
N2

## Slide 32: Construction- Core Type
Yoke
LV winding
Insulation
Limbs
Core
Winding crossover
Primary &
Secondary windings
Laminations
Notes: Picture courtesy: google.com

## Slide 33: Construction- Shell Type
Side Limb
Central Limb
LV winding
Insulation
HV winding
Yoke
Core
Insulation
Secondary
Winding
Yoke
Terminals
Laminations
Notes: Picture courtesy: google.com

## Slide 34: Losses & Efficiency
Core Loss
    Hysteresis Loss
    Eddy Current Loss
  Depends on flux which is constant hence the loss is constant
  Minimized using high graded core material and lamination
Copper Loss
    Winding Resistance (in primary and secondary)
  Current (or Load) dependent, hence variable loss
Total Loss = Core Loss + Copper Loss
Efficiency: Very high 97% to 99% (since it is a static device)

## Slide 36: Auto Transformer
One winding transformer
  Part of winding common to primary & secondary circuits
One winding wound over the entire core
Secondary winding can be varied using variable point
Used in power applications to interconnect systems operating at different voltage classes, for example 138 kV to 66 kV for transmission
Primary winding
N1 turns
Supply side
Load side
Secondary winding
N2 turns
Variable point
Supply side
Load side
Notes: Picture courtesy: google.com
Picture courtesy: google.com

## Slide 37: Auto Transformer- Types
LOAD
LOAD
Primary N1
Secondary N2
N1 > N2 : Step Down type
N1 < N2 : Step Up type

## Slide 38: 3 Phase Transformer
3 primary coils & 3 secondary coils.
Possible connections of primary & secondary windings:
star/star
  star/delta
  delta/delta
  delta/star
3 single-phase transformers of similar ratings can be connected to form a 3 phase transformer
Notes: Picture courtesy: google.com

## Slide 39: Application
Power Transformer: Used in electric transmission network
Distribution Transformer: Used in electric distribution networks
Instrument Transformers (PT & CT): Used for high voltage & current measurement
Isolation Transformer: 1:1 transformers used in circuits to provide electrical isolation.
Constant Voltage Transformer: Used as voltage regulators
High frequency Transformer: Transformers designed for operating with high frequency – ferrite core