## Slide 1: Basic Electrical Technology [ELE 1051]
L27 – Electrical Machines (DC Motors & AC Motors)

## Slide 2: Introduction to Electric machines
Electric motors may be broadly classified as
  D.C motors
  Induction motors
  Synchronous motors
The last two categories of motors operate on alternating current.
Both ac and dc motors work with the Law of electro magnetic induction and Law of electromagnetic interaction such as Faraday’s law, Lenz’s law, Ampere's law, Biot-Savart’s law etc…
Dept. of Electrical & Electronics Engg., MIT - Manipal

## Slide 3
DC Motors
Dept. of Electrical & Electronics Engg., MIT - Manipal

## Slide 5: Construction
Major parts are the stator and the rotor with an air gap in between.
  Stator : houses the field winding
  Rotor : carries the armature winding
Stator consists of
  Yoke(or frame)
  Poles
  Brushes, brush holders and end covers
Rotor consists of
  Armature
  Commutator
Dept. of Electrical & Electronics Engg., MIT - Manipal

## Slide 6: Construction
Yoke
Outer shell housing all the parts
Two end covers supporting the bearings
Cast steel is used as a material
Main Poles
The field coils are wound
When excited with dc , produce alternate North and South poles
Dept. of Electrical & Electronics Engg., MIT - Manipal

## Slide 7: Construction
Armature
Rotating part of the DC machine.
Core is slotted to receive the armature winding.
Commutator
Mechanical Rectifier which rectifies AC to DC
Carbon Brushes rest on the surface of the commutator.
The brush holders provide slots for the brushes to be placed
Armature
coils
Brush
Commutator
Dept. of Electrical & Electronics Engg., MIT - Manipal

## Slide 8: Working Principle
Dept. of Electrical & Electronics Engg., MIT - Manipal

## Slide 9: Working Principle
Current carrying armature conductors placed in the magnetic field experience a force which rotates the armature.
Induced emf in armature conductor regulates the current drawn to match with the connected load.
The motor continues to operate in an equilibrium with motor torque balancing load torque and the tractive effort.
Dept. of Electrical & Electronics Engg., MIT - Manipal
V = Voltage applied(Volts)
Eb = Induced Back e.m.f(Volts)
Ia = Armature current(Amperes)
Ra = Armature resistance(ohms)
N = Speed of the motor(r.p.m)
T = Torque developed(Nm)
Ø = Flux (Webers)

## Slide 12: Types of DC Motors
Shunt-Wound.
Series-Wound.
Compound-Wound.
Separately excited DC motor.
Dept. of Electrical & Electronics Engg., MIT - Manipal

## Slide 13: Types of DC Motors
DC Shunt Motor
Torque proportional to armature current.
Currents in the field and armature are independent of one another.
As a result, these motors have excellent speed control.
Dept. of Electrical & Electronics Engg., MIT - Manipal
Speed Torque characteristics

## Slide 14: Types of DC Motors
DC Series Motor
Field and armature currents are equal
Torque is proportional to the square of the armature current
Starting torque quite high and its gets regulated automatically as speed increases.
Most preferred for Traction.
Dept. of Electrical & Electronics Engg., MIT - Manipal
Speed Torque characteristics
Speed
Torque

## Slide 15: Types of DC Motors
DC compound motor Seperately excited DC motor
Dept. of Electrical & Electronics Engg., MIT - Manipal

## Slide 16: Applications
D.C. shunt motor is used for drive requiring moderate torques.
D.C. series motor: Electric traction, high speed tools
D.C. compound motor :Rolling mills and other loads requiring large momentary torques
Dept. of Electrical & Electronics Engg., MIT - Manipal

## Slide 17: Summary
D.C Motors can be shunt wound , series wound , compound wound or separately excited .
  For a d.c motor

## Slide 18: Basic Electrical Technology [ELE 1051]
L27- AC motors

## Slide 19
Induction Motors
Dept. of Electrical & Electronics Engg., MIT - Manipal

## Slide 20: Introduction
Nearly 80% of the world’s ac motors are poly-phase induction motors.
It has simple and rugged construction.
It is available from fractional horsepower ratings to megawatt levels.
There are machines available to operate from 3 phase or single phase electrical input
Single phase induction motors are restricted to small power levels (say less than 2 hp)
3 phase induction motors are widely used as pump & fan drives
For all practical purpose, it may be considered as a constant speed drive with full load slip around 3 %.
Dept. of Electrical & Electronics Engg., MIT - Manipal

## Slide 21: Construction
Dept. of Electrical & Electronics Engg., MIT - Manipal
Rotor
Stator

## Slide 22: Construction
Stator
Stator frame (cast iron) provides mechanical support to the stator core
Stator core laminated and slotted to carry the 3 phase windings
The balanced windings are displaced in space by 120 degrees electrical
Dept. of Electrical & Electronics Engg., MIT - Manipal
Stator core
Stator windings

## Slide 23: Construction
Types on the basis of rotor construction
  Squirrel Cage Rotor
  Slip Ring Rotor
Cylindrical Laminated core
Slots cutout on outer periphery
Conductors placed in slots
Dept. of Electrical & Electronics Engg., MIT - Manipal

## Slide 24: Construction
Wound Rotor
rotor winding is uniformly distributed and is usually connected in star.
The terminals of the winding are brought out to three slip rings
Slip rings in contact with brushes
Brushes connected to external resistance for higher starting torque
Dept. of Electrical & Electronics Engg., MIT - Manipal

## Slide 25: Working Principle
3-phase currents flowing in the stator winding produce a rotating
magnetic field rotating at synchronous speed.

## Slide 26: Working Principle
Dept. of Electrical & Electronics Engg., MIT - Manipal
Stator
Rotor
Direction of rotation of magnetic field
Rotating magnetic field
Rotor
Rotating magnetic field is cut by the rotor conductor
EMF is induced in rotor conductor
Current in the rotor conductor sets up a magnetic field which opposes the rotation of main field
Main field is independent and hence rotor field tries to catch up the speed of main field to reduce the relative speed
Rotor rotates in the same direction as that of rotating magnetic field

## Slide 27: Working Principle
Dept. of Electrical & Electronics Engg., MIT - Manipal
The axis of the magnetic field rotates at a synchronous speed
NS = Speed of RMF, rpm
f = Frequency of ac supply, Hz
P = No. of poles
NS = Synchronous Speed,rpm
N = rotor speed, rpm
If N = NS,
  No flux cut by rotor conductors
  No emf induced across rotor conductors
  No current flow, no torque
Hence N < Ns must for rotor rotation

## Slide 28: Working Principle
Dept. of Electrical & Electronics Engg., MIT - Manipal
Slip speed = (NS – N), rpm
For rotor speed N, relative speed = NS - N
Note
At instant of starting, N = 0, s =1 , fr = f

## Slide 29: Speed-Torque Characteristics
Dept. of Electrical & Electronics Engg., MIT - Manipal
Torque(Nm)`
Braking or Plugging
Motoring
Generating
or
re-generative braking
Slip
Speed(rpm)

## Slide 30: Applications
Industrial & Commercial Applications
  Pumping Systems
  Refrigeration Systems
  Compressors
  Fans & Blowers
  Industrial Drives
Dept. of Electrical & Electronics Engg., MIT - Manipal

## Slide 31
Single Phase Induction Motor
Dept. of Electrical & Electronics Engg., MIT - Manipal

## Slide 32: Introduction
Construction is similar to 3 phase induction motor except the stator has TWO winding - starting & running.
The rotor is of squirrel cage type
A capacitor is connected in series with the starting winding to achieve phase split.
The motor is started as two phase machine.
Dept. of Electrical & Electronics Engg., MIT - Manipal

## Slide 33
Dept. of Electrical & Electronics Engg., MIT - Manipal
Stator
Rotor
Construction

## Slide 34: Working Principle –Double field revolving theory
Resultant field is alternating. Hence,
Single Phase induction motors are Not Self Starting in nature
Dept. of Electrical & Electronics Engg., MIT - Manipal
Torque, Nm
Slip, %
0
0.5
1
1.5
2
Torque due to forward field TF
Torque due to reverse field TB
Resultant Torque

## Slide 35: Starting
The motor is started as two phase induction motor
Phase split is achieved by connecting a series capacitor with starting winding
Types
Capacitor Start Motor – pump / compressor motors
Capacitor Run Motor – ceiling fan motor
Dept. of Electrical & Electronics Engg., MIT - Manipal

## Slide 36: Capacitor Start Motor
Centrifugal Switch opens the circuit when speed is near about rated speed
Capacitor present in circuit only at starting
Dept. of Electrical & Electronics Engg., MIT - Manipal
Main Winding
Rotor
Starting Winding
Capacitor
Centrifugal
Switch
V
I1
Ist
Im
st
m
V
Ist
Im
I1

## Slide 37: Applications
Low power applications such as Air conditioners, Pumps, Fans.
Refrigerators, Washing Machines etc…
Dept. of Electrical & Electronics Engg., MIT - Manipal

## Slide 38: Summary
Three phase Induction motors have inherent self- starting torque . It can never run at synchronous speed.
Single phase Induction motors are used for small power applications The common forms are capacitor start and capacitor run motor.
Dept. of Electrical & Electronics Engg., MIT - Manipal