## Slide 1: PART II DIGITAL ELECTRONICS
Reference
Malvino and Leach, Digital Principles & applications, 7th edition, TMH, 2010
Morris Mano, “Digital Design”, Prentice Hall of India, Third Edition.
Chapter 4 : Number systems and Codes

## Slide 2: Module 1 : Number systems
Learning outcomes
At the end of this module, students will be able to:
Describe the decimal, binary, hexadecimal and octal system.
Convert the number in binary, octal or hexadecimal to a number in the decimal system and vise versa.
Describe the binary arithmetic using ones and two’s complement

## Slide 3: Introduction
Why Number System
Importance of Number system in electronics

## Slide 4: Number System
The different number systems are:
  Decimal system
  Binary system
  Hexadecimal system
  Octal system

## Slide 5: Decimal System
10 symbols, namely 0,1,2,3,4,5,6,7,8 and 9.
Example: (781)10, (6543.124)10
6543.124
Digit | 6 | 5 | 4 | 3 | . | 1 | 2 | 4
Weight | 103 | 102 | 101 | 100 | Decimal Point | 10-1 | 10-2 | 10-3

## Slide 6: Binary System
Uses only two symbols ‘0’and’1’ .
Radix-2 system. Example: (100010)2, (1011.101)2.
Digit | 1 | 0 | 1 | 1 | . | 1 | 0 | 1
Weight | 23 | 22 | 21 | 20 | Binary Point | 2-1 | 2-2 | 2-3
1011.101

## Slide 7: Hexadecimal System
The hexadecimal number system has base 16.
It has 16 distinct symbols. It uses the digits 0-9 and letters A,B,C,D, E and F as 16 symbols.
Example:
Digit | 4 | A | 9 | 0 | . | 2 | B | C
Weight | 163 | 162 | 161 | 160 | Hexadecimal Point | 16-1 | 16-2 | 16-3
4A90.2BC

## Slide 8: Octal System
Uses 8 symbols (0-7)
Example: (723)8, (2157.075)8.
Digit | 2 | 1 | 5 | 7 | . | 0 | 7 | 5
Weight | 83 | 82 | 81 | 80 | Octal Point | 8-1 | 8-2 | 8-3

## Slide 9: Self Test
The hex numbering system has a base of ________, and the binary numbering system has a base of ________.
The value of a particular digit in a number is determined by its relative position in a sequence of digits. (T/F)
A single hexadecimal digit can represent how many binary digits: (a) two, (b) three, or (c) four?
The bases of the binary and decimal numbering systems are multiples of 2. (T/F)

## Slide 10: Conversion of Number System
  Decimal
    Decimal to Binary
    Decimal to Octal
    Decimal to Hexadecimal
  Binary
    Binary to Octal
    Binary to decimal
    Binary to Hexadecimal
  Octal
    Octal to binary
    Octal to decimal
    Octal to Hexadecimal
  Hexadecimal
    Hexadecimal to Binary
    Hexadecimal to Octal
    Hexadecimal to decimal

## Slide 11: Conversion
Decimal System

## Slide 12: Decimal to Binary
The given decimal number is repeatedly divided by 2.
Till quotient becomes ‘0’ .
Remainder is collected from bottom to top.
Real Part:
Fractional part is multiplied by two repeatedly.
The integer part is recorded.
The string of integer obtained from the top to bottom gives the equivalent fractional number in binary
Fractional Part:

## Slide 13: Decimal to Binary
37 | divided by | 2 | Q=18 | R=1
18 | divided by | 2 | Q=9 | R=0
9 | divided by | 2 | Q=4 | R=1
4 | divided by | 2 | Q=2 | R=0
2 | divided by | 2 | Q=1 | R=0
Q1. (37)10 = (100101)2

## Slide 14
Q2. =

## Slide 15
Q3. =

## Slide 16
Q4. =

## Slide 17: Decimal to Octal
The given decimal number is repeatedly divided by 8.
Till quotient becomes ‘0’ .
Remainder is collected from bottom to top
Real Part:
Fractional part is multiplied by eight repeatedly.
Carry in the integer place is recorded.
The string of integer obtained fro m the top to bottom gives the equivalent fractional number in octal
Fractional Part:

## Slide 18: Decimal to Octal
Ex: (97)10 = (141)8
37 | divided by | 8 | Q=12 | R=1
12 | divided by | 8 | Q=1 | R=4

## Slide 19
Q5. =

## Slide 20: Decimal to Hexadecimal
The given decimal number is repeatedly divided by 16.
Till quotient becomes ‘0’ .
Remainder is collected from bottom to top
Real Part:
Fractional part is multiplied by sixteen repeatedly.
Carry in the integer place is recorded.
The string of integer obtained fro m the top to bottom gives the equivalent fractional number in hexadecimal.
Fractional Part:

## Slide 21: Decimal to Hexadecimal
Ex: (546)10 =(222)16
546 | divided by | 16 | Q=34 | R=2
34 | divided by | 16 | Q=2 | R=2

## Slide 22
Q6. =

## Slide 23: Conversion
Binary System

## Slide 24: Binary to Octal
Ex1: (110101010)2 =
110 101 010 =
6 5 2 = (652)8
Ex2: (0.1011010)2 =
101 101 0
5 5 0 = (0. 550)8
Ex3: (110101010. 1011010)2 = (652.550)8
Each octal digit is represented by three bits of binary digits.

## Slide 25
Q7. =

## Slide 26: Binary to Decimal
Multiply the number by its equivalent binary weights.
Add the products to get the decimal number.
Ex1: 1102 = 1 x 22 + 1 x 21 + 0 x 20 = 4 +2+0 = 6
Ex2: 0.1012 = 1 x 2-1 + 0 x 2 -2 + 1 x 2-3 = 0.5 + 0 + 0.125 = 0.625

## Slide 27
Q7. =

## Slide 28: Binary to Hexadecimal
Ex1: (111110110010)2 =
1111 1011 0010
15 11 2
F B 2
(FB2)16
Ex2: (0.010101111011)2
0101 0111 1011
5 7 11
5 7 B
(0.57B) 16
Each group of 4 binary bits is 1 hexadecimal digit.

## Slide 29
Q8. =

## Slide 30: Conversion
Octal System

## Slide 31: Octal to Binary
Ex1: (347)8 = (011100111)2
Ex2: (0.245)8 = (0.010100101)2
Ex3: 347.2458 = (011100111.010100101)2
Each octal digit is represented by three bits of binary digit.

## Slide 32
Q9. =

## Slide 33: Octal to Decimal
Ex1: (457)8 = 4 x 82 + 5 x 81 + 7 x 80 = 4 x 64 + 5 x 8 + 7 x 1 = 256+40+7 = (303)10
Ex2: (0.246)8 = 2 x 8-1 + 4 x 8-2 + 6 x 8-3= 2 x 0.125 + 4 x 0.015625 + 6 x 0.001953125
= (0.267969)10
Multiply the number by its equivalent octal weights.
Add the products to get the decimal number.

## Slide 34
Q10. =

## Slide 35: Octal to Hexadecimal
Ex1: (235)8 = (09D)16
(235)8 = (0 1001 1101)2 = (09D)16
The octal number is first converted into binary.
The binary bits are grouped such that each group consists of 4 bits and a group starts from the LSB.
The 4 bits group is represented by its equivalent hexadecimal number.

## Slide 36
Q11. =

## Slide 37: Conversion
Hexadecimal System

## Slide 38: Hexadecimal to Binary
Ex1: (A7D)16 = (1010 0111 1101)2
Each group of 4 binary bits is 1 hexadecimal digit.

## Slide 39
Q12. =

## Slide 40: Hexadecimal to Octal
Ex1: (C4)16 = (11 000 100)2= (304)8
Ex2: (0.26A)16 = (0.001 001 101 010)2 =(0.1152)8
Ex3: (C4.26A)16 = (11 000 100.001 001 101 010)2 = (304.1152)8
The hexadecimal number is first converted into binary.
They are grouped into 3 bits each starting from the LSB.
The 3 bits group is represented by its equivalent octal number.

## Slide 41
Q13. =

## Slide 42: Hexadecimal to Decimal
Ex1: (B40)16 = 11 x 162 + 4 x 161 + 0 x 160
= 11 x 256 + 4 x 16 + 0 x 1
=(2880)10
Ex2: (0.237)16 = 2 x 16-1 + 3 x 16-2 + 7 x 16-3
= (0.138427)10
Multiply the number by its equivalent hexadecimal weights.
Add the products to get the decimal number.

## Slide 43
Q14. =

## Slide 44: Number System Arithmetic
Binary Addition
Ex1: (1010)2 + (0111)2 = (10001)2
(1010)2 = (10)10
+(0111)2 = (7)10
(10001)2 = (17)10

## Slide 46: Number System Arithmetic
Ex1: Add ( 334.65)8 to (671.14) 8 = 1226.018
Octal

## Slide 48: Number System Arithmetic
Hexadecimal
Add (7AB.67)16 to (15C.71) 16 = (907. D8)16

## Slide 50: 1’s and 2’s Complement
To find 1’s complement of a binary number just invert the bits.
To find 2’s complement of a binary number find 1’s complement and add 1 to the result.
1’s complement of 0011 is 1100.
2’s complement of 0110 is 1010.

## Slide 51: Subtraction using 1’s complement method
1)Add minuend to the 1’s complement of subtrahend
2)Check the result obtained in step 1 for any carry
a)If an end carry occurs, add it to the LSB
b)If an end carry doesn’t occur, get the 1’s complement of the answer obtained in step 1 and place a negative sign before it.

## Slide 52: Subtraction using 2’s complement method
1)Add minuend to the 2’s complement of subtrahend
2)Check the result obtained in step 1 for any carry
a)If an end carry occurs, discard it
b)If an end carry doesn’t occur, get the 2’s complement of the answer obtained in step 1 and place a negative sign before it.

## Slide 53
Ex1: Subtract (0011)2 from (0101)2 using 1’s complement.
Step1: 0101 is minuend and 0011 is subtrahend.
Step2: 1’s complement of 0011 is 1100.
Step3: 0101 + 1100 = 1 0001(there is a carry)
Step4: 0001 + 1 = 0010 (5 – 3 =2)

## Slide 60: Exercise
Subtract 14 from 46 using the 2’s complement method.
Subtract 35 from 23 using 2’s complement.